Developing Machine Learning Algorithms for Inferring Upstream Separatrix Density at JET
A. Kit, A.E. Järvinen, Y. Poels, S. Wiesen, L. Frassinetti, ENR-08 Team, and JET contributers
25th International Conference on Plasma Surface Interactions in Controlled Fusion Devices, June 13 – 17, 2022, Korea
E-mail: adam.kit@helsinki.fi
Link to poster:

---
A turing test
A turing test, one of these profiles was generated using deep learning, and one is real

---
A turing test, one of these profiles was generated using deep learning, and one is real
REAL
GENERATED

---
Through representation learning we construct a compressed representation of the plasma state
Learn a manifold of all possible plasma solutions in the latent space

---
Through representation learning we construct a compressed representation of the plasma state
Decoding the latent space, we retrieve representation of plasma solution
(profiles & machine parameters)
Latent space
Decoded profile

---
Through representation learning we construct a compressed representation of the plasma state
Decoding the latent space, we retrieve representation of plasma solution
(profiles & machine parameters)
Input machine parameters to
generate profiles
Latent space
Decoded profile

---
Through representation learning we construct a compressed representation of the plasma state
Decoding the latent space, we retrieve representation of plasma solution
(profiles & machine parameters)
Input machine parameters to
generate profiles
Control applications!

---
ML Problem setup and results
We also build a model for a direct mapping to nesep
X: Machine parameters
Plasma current, toroidal field, q95
Upper & lower triangularity, elongation
Major & minor radius, plasma volume,
Ohmic & NBI & ICRH power,
Gas puff,
f: X -> n_{ e, sep }